## Slide 1
Dual-Branch Network Design & Implementation
Enhancing Connectivity, Security, and Scalability

## Slide 2
Project Overview & Objectives
Goal
Design and simulate a secure, scalable dual-branch network using Cisco Packet Tracer.
Key Deliverables:
Seamless connectivity between Branch 1 & Branch 2.
Robust security (ACLs, Port Security) and redundancy (STP).
Core services implementation (DHCP, DNS, NAT).

## Slide 3
Strategic Network Planning
Presented by Mesk Khaled - Network Planning
Designing the Traffic Flow
Analyzed organizational needs and enforced VLAN segmentation (HR, IT, Sales) to isolate traffic and enhance security.
Implemented a VLAN strategy (VLANs 10, 20, 30, etc.) to isolate broadcast domains and improve security.
IP Addressing Architecture
Designed a Class C (/24) addressing scheme, providing 254 usable IPs per VLAN to accommodate future growth without reconfiguration.
Standardization & Blueprinting
Established strict naming conventions and Gateway standards to ensure consistency.
Defined the "Router-on-a-Stick" topology to enable efficient Inter-VLAN routing.

## Slide 4
Network Architecture & Topology
Presented by Basmala Moataz - Topology Design
Dual-Branch Setup
Understanding the two-branch structure (Branch 1 & Branch 2) and their unique requirements.
Core Components
Each branch features a Cisco 2911 Router for inter-VLAN routing, WAN link, NAT, DHCP/DNS, and Cisco 2960 Layer 2 Switches for VLAN segmentation and redundancy.
End Devices & Services
PCs for HR, IT, and Sales departments, along with a shared Web Server in Branch 1 hosting DNS, DHCP, and Web services.
WAN Link
A critical serial connection established between Branch 1 and Branch 2 routers for seamless communication.
My contribution focuses on translating the abstract network plan into a precise, visual, and functional model within Cisco Packet Tracer.

## Slide 5
Implementation Environment:
Cisco Packet Tracer
Presented by Asmaa Mahmoud - Packet Tracer Setup
Tool Overview & Device Placement
Cisco Packet Tracer served as our primary simulation environment, allowing for virtual device deployment and organization.
Physical Interconnections
PC to Access Switch: Straight-through cables.
Inter-Switch Redundancy: Crossover cables with STP enabled.
Router-to-Switch Uplinks: GigabitEthernet, straight-through cables.
WAN Connection: Serial DCE/DTE cables after module installation.
Naming Conventions
Consistent device naming was crucial for clarity and streamlined teamwork throughout the project.
My role involved meticulously bringing the network design to life within the simulation, ensuring proper physical connectivity and configuration readiness.

## Slide 6
VLAN Implementation & Inter-VLAN Routing
Presented by Ziad Yasser - VLAN Configuration
Purpose of VLANs
VLANs improve network performance, security, and effectively segment broadcast domains, preventing network congestion.
VLAN Structure
Branch 1: VLAN 10 (HR), VLAN 20 (IT), VLAN 30 (Sales). Branch 2: VLAN 40 (HR), VLAN 50 (IT), VLAN 60 (Sales).
Port Assignment
Switch ports were meticulously assigned to specific VLANs (e.g., Fa0/1-6 for HR VLAN 10) to ensure logical separation.
Inter-VLAN Routing
Router sub-interfaces with 802.1Q encapsulation act as gateways, allowing communication between departments while maintaining logical separation.
Verification
Utilising the show vlan brief command confirmed correct VLAN configurations and port assignments across all switches.
My focus was on logically segmenting the network and enabling controlled, efficient communication between these distinct segments.

## Slide 7
IP Addressing & Core Network Services
Presented by Mohamed Amgad - DHCP, DNS, NAT
IP Address Planning
/24 subnets were chosen for each VLAN (e.g., 192.168.1.0/24 for HR Branch 1), providing sufficient addresses and simplified management. WAN link IPs were set as 10.0.0.0/24.
DHCP Configuration
Dedicated DHCP pools for each VLAN ensure automatic IP address assignment for client devices, including mask, gateway, and DNS server details, enhancing network efficiency.
DNS Configuration
A shared server in Branch 1 acts as the DNS server, enabling human-readable domain names (e.g., www.company.local) for easy access.
NAT Implementation
Network Address Translation (NAT) allows private IP addresses within our network to access the public internet, demonstrated through show ip nat translations.
My responsibility was to ensure efficient and seamless network communication through automated addressing, reliable name resolution, and external connectivity enablement.

## Slide 8
Implementing Network Security Measures
Presented by Adham Ashraf - ACL, Port Security
Access Control Lists (ACLs)
Objective: Enforce a "Least Privilege" security model.
Implementation: Extended ACL 100 applied inbound on the Sales sub-interface.
Rules Example: Deny Sales access to HR and IT, permitting all other traffic (e.g., internet access).
Verification: Using show access-lists and ping tests confirmed ACL effectiveness, blocking unauthorised inter-departmental communication.
Port Security
Objective: Prevent unauthorised devices from connecting to access ports.
Implementation: Configured on access switch ports (Fa0/1-23).
Settings: Maximum 1 MAC address, violation mode set to shutdown, with sticky MAC learning for dynamic and secure port management.
Verification: Successfully demonstrated port shutdown upon security violation, validated by show port-security output.
My role in fortifying the network against unauthorised access and ensuring data integrity at both Layer 2 and Layer 3 was crucial for project success.

## Slide 9
Ensuring Network Resilience
Presented by Adham Ashraf - Testing
Spanning Tree Protocol (STP)
STP prevents switching loops in redundant Layer 2 paths, ensuring network stability and preventing broadcast storms. It automatically blocks redundant links.
High Availability
STP ensures high availability by activating backup links if a primary link fails, guaranteeing continuous network operation without manual intervention.
Broadcast & Collision Domains
VLANs and switches efficiently manage broadcast and collision domains, reducing network traffic and enhancing overall performance and stability. We identified 7 broadcast domains (6 VLANs + 1 WAN).
My focus was on validating the robustness of the network, including the critical fault tolerance mechanisms that ensure continuous operation.

## Slide 10
Validation & Proof of Concept
Presented by Adham Ashraf - Testing
Physical Connectivity
All links verified as "green" in Packet Tracer, confirming successful physical interconnections across the network.
Inter-VLAN & Inter-Branch
Successful ping tests confirmed seamless communication both between different VLANs within a branch and between devices in separate branches.
Service Access
DHCP clients successfully obtained IPs, DNS allowed web access to www.company.local, and NAT enabled internet access for private networks.
Security Validation
ACLs effectively blocked Sales from HR/IT, and port security successfully triggered a port shutdown upon an unauthorised device connection.
Redundancy
Simulated link failure demonstrated STP's rapid convergence, highlighting the network's resilience and fault tolerance capabilities.
Systematic verification ensured all implemented configurations functioned as intended and comprehensively met the project objectives.

## Slide 11
Project Success & Conclusion
Summary of Achievements
We successfully designed and implemented a fully functional dual-branch network solution.
Connectivity: Validated seamless communication via OSPF routing and Inter-VLAN routing.
Security: Enforced robust access control via Port Security and ACLs.
Services: Successfully deployed active DHCP, DNS, and NAT configurations.
Key Learnings
Through this project, we moved beyond theory to practical application. We mastered the integration of switching, routing, and security protocols into a unified architecture and developed critical troubleshooting skills for resolving complex network conflicts.

## Slide 12
Thank You!
Any Questions?